## Slide 1: Non Dimensional Numbers in Motion of Fluids and their Significance Fluid Mechanics (DTE 112)
Dr. J. Badshah
University Professor – cum - Chief Scientist
Dairy Engineering Department
Sanjay Gandhi Institute of Dairy Science & Technology, Jagdeopath, Patna
(Bihar Animal Sciences University, Patna)

## Slide 2: Inertia Force and Reynolds Number
Introduction
Inertia Force : Important for Fluids in Motion
  Inertia Force Fi = Mass x Acceleration
  Fi = Density x volume x Velocity per unit time
  = Density x volume per unit time x velocity
  = Density x Area x velocity x Velocity
  = ℓ L2 v2
Non dimensional Numbers: Using above relation of inertia force for the fluid in motion, it is interesting to develop the ratio of inertia force to each of the other forces, which are known as non-dimensional numbers.
Reynolds Number NRe: Ratio of Inertia Force to viscous Force = ℓ L2 v2 / mue du/dy x A = ℓ L2 v2 / µ v L = ℓ v L/ µ
Significance: Reynolds Number is used to determine and correlate pipe friction coefficient, Drag coefficient, Discharge coefficient etc.

## Slide 3: Froud Numbers & significance
  Froud Number, NF: Square root of the Ratio of Inertia Force and gravity Force = √Fi / Fg = √ ℓ L2 v2 /mg = √ ℓ L2 v2 / ℓ L3 g
  NF = v/ √ L g
Significance
It is important in open channel flow.
It is useful in study of hydraulic jump.
It is used in design of hydraulic structures
It is used in design of ship
It is used in design of agitators and mixers for liquids.

## Slide 4: Cauchy Number & Significance
Cauchy Number, Nc : The ratio of inertia force and elasticity force = Inertia Force/Elasticity Force
= ℓ L2 v2 / Bulk modulous x area
= ℓ L2 v2 / K L2 = v2 / K/ ℓ
Significance
The Cauchy number (Ca) is a dimensionless number in continuum mechanics used in the study of compressible flows. It is named after the French mathematician Augustin Louis Cauchy.
When the compressibility is important the elastic forces must be considered along with inertial forces for dynamic similarity.

## Slide 5: Mach Numbers and Significance
Mach Number: It is the square root of the ratio of inertia force to elasticity force. It is also the square root of Cauchy Number
Mach No. NM = √ ℓ L2 v2 / K L2 = v/ √K/ ℓ
It is also defined as the ratio of the velocity of the object relative to the fluid to the velocity of the sound in that fluid such as in case of aircraft in flight. Mach numbers less than one indicate subsonic flow; those greater than one, supersonic flow.
It is important in compressible fluid flow problems at high velocity such as motion of high speed projectiles and missiles. Fluid flow is classified as compressible or incompressible on the basis of the Mach number. For example, gas flowing with a Mach number of less than three-tenths may be considered incompressible, or of constant density, an approximation that greatly simplifies the analysis of its behaviour.

## Slide 6: Mach Numbers and Significance
It is important in high velocity flow in pipes, pumps, separators, homogenizers, compressors, turbines etc.
It is important in design of sound proof auditorium and big halls.
For Mach numbers greater than one, shock wave patterns develop on the moving body because of compression of the surrounding fluid. Streamlining alleviates shock wave effects.

## Slide 7: Weber Number and Significance
  Weber Number: It is the square root of the ratio of inertia force to Surface tension force.
  Weber Number, We or Nw = √ ℓ L2 v2 / σ L = v / √ (σ/ ℓ L)
  Significance
  The Weber number (We) is a dimensionless number in fluid mechanics that is often useful in analysing fluid flows where there is an interface between two different fluids, especially for multiphase flows with strongly curved surfaces. It is named after Moritz Weber (1871–1951).
  It is important for design of nozzles, jets and atomizers
  It is important for formations of droplets and enhancing surface area of liquid
  It is important in formation of waves in different applications of high velocity flow of air, gases and liquid

## Slide 8: Euler Number and Significance
Euler Number: It is the ratio of the pressure force to the inertia force
Euler Number, Eu or NE = (Pu –Pd) L2 / ℓ L2 v2 = (Pu –Pd) / ℓ v2
Significance
It is important in flow problems in which a pressure gradient exists in flow.
It expresses the relationship between a local pressure drop caused by a restriction and the kinetic energy per volume of the flow.
It is used to characterize energy losses in the flow, where a perfect frictionless flow corresponds to an Euler number of 1. The inverse of the Euler number is referred to as the Ruark Number with the symbol Ru.
Cavitation number[edit]
The cavitation number has a similar structure, but a different meaning and use:
The Cavitation number (Ca) is a dimensionless number used in flow calculations. It expresses the relationship between the difference of a local absolute pressure from the vapor pressure and the kinetic energy per volume, and is used to characterize the potential of the flow to cavitate.

## Slide 9: Cavitation Number and Significance
Cavitation Number: The Cavitation number (Ca) is a dimensionless number used in flow calculations.
  Cavitation Number, Ca = p – pv / ½ ℓ v 2
  p = Local pressure
  pv = Vapour pressure of fluid
  ℓ = Density of the fluid
  v = Characteristic velocity of flow of fluid
Significance
  It expresses the relationship between the difference of a local absolute pressure from the vapor pressure and the kinetic energy per volume, and is used to characterize the potential of the flow to cavitate.
  It helps in design of pumps and turbine.
  It helps in design of flow of hot liquid/ steam/ condensate in pipes/conduits.

## Slide 10
THANK YOU